## Slide 1
StructLabPro
An Open-Source Desktop Structural Analysis Tool in Python
Direct Stiffness Method · 2D & 3D · PyQt6 GUI · Python SDK · GPL v3 Licence
Open Source Tools for Engineering — 2026
Imed Mhamdi
V 1.0.0 — First Public Release
1

## Slide 2
Agenda
Overview
2
01
The Open-Source Structural Analysis Landscape
What tools exist, their strengths and gaps
02
What is StructLabPro?
Architecture, scope, and design decisions
03
Features Walkthrough
Modelling, results, Python SDK — with live demo
04
Validation
20 benchmark cases vs OpenSeesPy & analytical solutions
05
V1.0 Scope Boundaries
What this release does not do
06
Roadmap & Contributing
Where the project goes next

## Slide 3
Open-Source Structural Analysis Tools
A survey of what exists before StructLabPro
Landscape
3
Tool
Domain
Interface
Key Strength
Key Limitation
OpenSees / OpenSeesPy
Frame + Continuum FEM
Python / Tcl scripting
Nonlinear, dynamic, seismic — research-grade
No GUI, steep learning curve, no interactive modelling
Frame3DD
3D frames & trusses
CLI + text file
Lightweight, fast, well-validated
No GUI, dated UX, limited load types, no Python API
PyNite
3D frame / truss
Python library
Clean modern Python API, MIT licence
Library only — no GUI, no visual workflow
anastruct
2D frames
Python library
Simple Pythonic API, quick to learn
2D only, limited loads, no GUI
FEniCS / FEniCSx
Continuum FEM
Python
Very powerful for PDEs and continuum
Not designed for frame/beam structures
CalculiX
General FEM
CLI / PrePoMax GUI
Industrial-grade, Abaqus-compatible
No Python SDK, complex input, steep learning curve
* Table covers widely-used FOSS tools as of 2026; excludes commercial tools (SAP2000, ETABS, RFEM, Abaqus).

## Slide 4
The Gap StructLabPro Addresses
Most tools are either GUI-only or scripting-only
Landscape
4
Scripting / programmable
GUI / interactive
Simple / educational
Powerful / research
OpenSees
PyNite
anastruct
Frame3DD
CalculiX
★ StructLabPro
StructLabPro targets the intersection:
· Full desktop GUI for interactive modelling
· Python SDK + embedded console for scripting
· GPL v3 licence, standalone .exe, zero install

## Slide 5
What is StructLabPro?
A 2D & 3D structural analysis desktop application
Project
5
Solver
Direct Stiffness Method — 2D (3 DOF/node) and 3D (6 DOF/node), unified engine
Elements
Beams · Frames · Trusses · Bars · Spring supports · Pin releases
Loads
Point loads · UDL · UVL · Nodal moments · EN 1990 load combinations
GUI
PyQt6 desktop application — dark theme, interactive canvas, overlays (BMD/SFD/AFD/deformed shape)
Sections
European steel section library (IPE, HEA, HEB, SHS, RHS) + custom sections
Output
Displacements · Reactions · Member forces · Design utilisation η · Multi-page PDF report
SDK
sdk.py Python API + embedded IPython console — model and solve without the GUI
Distribution
Standalone .exe via PyInstaller — no Python install required for end users
Licence
GPL v3 — free to use, modify, distribute (copyleft)

## Slide 6
Architecture — One Engine, All Structure Types
2D/3D is auto-detected; no separate solver per mode
Project
6
GUI Layer
PyQt6 canvas · Properties panel · Load case manager · Overlay diagrams
Model State
NodeData · MemberData · LoadCase · SupportType (pure Python dataclasses)
Model Builder
ModelState → core Model bridge · sub-node division for overlays · z-coord auto-detect
Core Engine
FrameElement (2D 6×6 / 3D 12×12) · Assembler · LinearSolver · Postprocessor · FEM loads
Python SDK / IPython Console
sdk.py · build models in pure Python · solve() · query results · matplotlib plots
NumPy · SciPy · Matplotlib underpin the engine. The GUI never bypasses the solver — it always goes through Model Builder → Core Engine.

## Slide 7
Modelling — Interactive Canvas
Draw structures directly or load from 30+ built-in presets
Features
7
Canvas
▸ Click to place nodes, drag to connect members
▸ Snap-to-grid, multi-select, Ctrl+D duplicate
▸ 2D and 3D modes — isometric projection, working planes (XY / XZ / YZ)
▸ Orbit, pan, zoom in 3D view
▸ Selection filter: nodes / members / both
Element Types
▸ Beam (continuous, with/without pin releases)
▸ Frame (rigid joints, full 3 or 6 DOF)
▸ Truss / Bar (pin at both ends)
▸ Spring supports (translational & rotational)
▸ Mixed models — beams + columns + trusses in one model
Loads & Cases
▸ Point loads (Fx, Fy, Fz, Moment)
▸ UDL and UVL (varying distributed) on members
▸ EN 1990 named load cases (G, Q, W, …)
▸ Load combinations with factors
▸ Combination envelope (max / min across all combos)
▸ Pattern loading detection (EN 1992-1-1)

## Slide 8
Results — Visual Overlays + Tabular Output
Live diagrams drawn directly on the canvas after solve
Features
8
BMD
Bending Moment Diagram — filled, sign-correct (sagging below baseline, hogging above)
SFD
Shear Force Diagram — peak values labelled at critical sections
AFD
Axial Force Diagram — compression / tension colour-coded
Def
Deformed Shape — scaled, shows buckled mode visually
Results Panel — four tabs:
▸ Displacements
dx, dy (mm) · θ (mrad) per node
▸ Reactions
Fx, Fy (kN) · M (kN·m) at supports
▸ Member forces
N, V end-pair + M+ peak sagging · M− peak hogging + x/L position
▸ Design
M_Ed vs M_Rd · utilisation η (%) · Pass / Fail status
Bidirectional selection:
Click a table row → highlights member on canvas
Click canvas member → scrolls to that row in table
PDF Report:
Multi-page A4 · geometry + loads + diagrams + full results table

## Slide 9
Python SDK & Embedded Console
The GUI and the scripting interface share the same live model
Features
9
sdk.py — build and solve in pure Python:
▸ No GUI needed — runs in any Python environment
▸ Same engine as the desktop app (single code path)
▸ Ideal for parametric studies, lecture examples, automated checks
▸ Results returned as typed Python objects (not strings)
Embedded IPython Console:
▸ Opens inside the running app (qtconsole)
▸ model, state, sdk, np, plt pre-injected
▸ Inspect, modify, or extend the current canvas model
▸ matplotlib plots open in separate windows
# Simply supported steel beam — 6 m, UDL 15 kN/m
import sdk
m = sdk.Model()
n0 = m.add_node(0, 0, 0)
n1 = m.add_node(6, 0, 0)
m.pin(n0)
m.roller(n1)
beam = m.add_member(n0, n1)
beam.set_section(E=210e9, A=5.381e-3, I=8.356e-5) # IPE 300
m.add_udl(beam, w=15_000) # 15 kN/m downward
res = m.solve()
print(res.max_deflection()) # → 7.03 mm
res.plot_bmd()

## Slide 10
Demo
10
Live Demonstration
1 · Launch → welcome dialog → load Steel Industrial Portal preset
2 · Add a load case · solve · walk through BMD / SFD overlays
3 · Generate PDF report
4 · Switch to 3D — open 3D Floor Grid preset · orbit · solve · deformed shape
5 · Open Python console · query model · plot BMD from the console

## Slide 11
Validation — 20 Benchmark Cases
StructLabPro vs OpenSeesPy (where applicable) and analytical solutions
Validation
11
ID
Type
Description
Reference
Max error
B1
Beam
Simply supported beam — midspan point load
Analytical (Euler-Bernoulli)
0.00%
B2
Beam
Propped cantilever — UDL
Analytical
0.00%
B3
Beam
Fixed-fixed beam — UDL
Analytical
0.00%
B4
Beam
3-span continuous beam — mixed loads
OpenSeesPy
0.00%
B5
Beam
Gerber beam — internal hinge (pin release)
Analytical
0.00%
F1
Frame
Simply supported portal — lateral load
OpenSeesPy
0.00%
F2
Frame
Fixed-base portal — UDL on beam
OpenSeesPy
0.00%
F3
Frame
Multi-storey frame — vertical + lateral loads
OpenSeesPy
0.00%
F4
Frame
Two-bay frame — asymmetric loading
OpenSeesPy
0.00%
F5
Frame
Pitched roof portal with eaves haunches
OpenSeesPy
0.00%
T1
Truss
8-panel Pratt truss — symmetric UDL
Method of joints
0.00%
T2
Truss
Warren truss — asymmetric point loads
Method of joints
0.00%
3D1
3D
3D cantilever — tip load in Y
Analytical
0.00%
3D2
3D
3D cantilever — tip load in Z
Analytical
0.00%
3D3
3D
3D simply supported beam — midspan load
Analytical
0.00%
3D4
3D
3D portal frame — in-plane lateral
OpenSeesPy
0.00%
3D5
3D
3D portal frame — out-of-plane lateral
OpenSeesPy
0.00%
3D6
3D
3D 2-storey space frame — combined loads
OpenSeesPy
0.00%
3D7
3D
3D floor grid — biaxial bending
OpenSeesPy
0.00%
3D8
3D
3D Pratt roof truss — space truss
Analytical
0.00%
All 20 cases: max displacement / reaction / moment error = 0.00% (tolerance < 0.01%)

## Slide 12
V1.0 — Scope Boundaries (What This Release Does Not Do)
Honest positioning — this is a linear-static desktop tool
Scope
12
Dynamic / Seismic
No modal analysis, no response spectrum, no time-history integration
Nonlinear Analysis
No geometric nonlinearity (P-Δ / large displacement), no material plasticity
Plates & Shells
Frame elements only — no 2D/3D continuum mesh elements
Design Code Checks
EC3 steel moment check (η = M_Ed/M_Rd) only — EC2 concrete check is a stub
Load Generation
Loads are manual — no EN 1991 wind, snow, or seismic auto-generator
Section Optimisation
Checks utilisation but does not select or size sections automatically
IFC / DXF Exchange
No import or export to BIM or CAD formats
Cloud / Multi-user
Local desktop only — no collaboration or cloud-hosted solve
Red = not in scope for V1.x · Amber = partial or planned

## Slide 13
Roadmap & Contributing
Open to contributions — GPL v3 licence on GitHub
Roadmap
13
Phase 10 (active)
3D modelling UX
Blender-style orbit · axis-constrained grab (G+X/Y/Z) · E-extrude · numpad view recall · 3D grid visual
Phase 11
EC2 Concrete Design Check
Steel / Concrete branch in Design tab · EC2 §6.1 rectangular stress block · user-input M_Rd for concrete
Phase 12
OpenSees Export
One-click export of any StructLab model to a ready-to-run OpenSeesPy script
Future
Dynamic / Nonlinear
Modal analysis · response spectrum · P-Δ geometric nonlinearity · pushover
How to contribute:
▸ Report bugs or request features via GitHub Issues
▸ Add benchmark cases — any textbook example with a known analytical solution
▸ Extend the SDK — new load types, result queries, export formats
▸ Improve the section library — EN 10365 profiles, CHS, angles, channels

## Slide 14
14
Thank You
StructLabPro V1.0.0 — Open Source Structural Analysis in Python
Licence:
GPL v3 — free to use, modify, distribute (copyleft)
Tech stack:
Python · NumPy · SciPy · PyQt6 · Matplotlib · PyInstaller
Solver:
Direct Stiffness Method · 2D & 3D unified engine
Tests:
92 / 92 passing · 20 benchmark cases · 0.00% error
Questions?